## Slide 1: Proaktives Verteilnetz - Proactive Distribution Grid
ETIP SNET Workshop
Aachen, September 18-19

## Slide 2: The majority of the new producers are connected to the distribution grids
There is a global trend for DER, Germany is one of the main applications
One of the key attributes of DER-generation is its volatility
There is also a trend for increasing flexibility and demand on the demand side
The usage of flexibility in supply&demand in distribution grids is necessary to guarantee a sustainable and reliable energy system
UHV
HV
MV
LV
Energiewende

## Slide 3: Traffic light concepts enable synergies between a market- and grid-driven usage of flexibility
The traffic light system is… |  |  | The traffic light system is not… | 
 | Indication of the actual status of grid <-> market interaction |  |  | Indication of the actual grid condition or available grid capacity
 | Market information of the actual usage of flexibility through DSOs |  |  | Information on the acutal grid stability and security of supply


Goals of the traffic light system
Open up flexibility
Resolving grid congestions
Expand energy grids at optimal (system) costs in the long term
Enhancing interaction of grid & market
Drivers
today
tomorrow
prospective
Fluctuating Feed-In
Higher coincidence
More consumption

## Slide 4: A valuable flexibility concept needs to incorporate grid and market interests in a common manner
  system oriented use balancing independent of location
  grid oriented use avoid local grid constraints
Flexibility adaption of generation or demand behavior by external signals
  market oriented use portfolio optimization of demand and supply
  Customer oriented use self-consumption

## Slide 5: Interaction of Market & Grid - Traffic light concept enables a flexible market environment
Green
Flexibility is offered by sales/ aggregators for market and system oriented portfolio optimisation and for balancing
Yellow
Flexibility is requested by DSO on a contractual basis to avoid economic inefficient network expansion
Red
Flexibility is controlled by DSO without contractual basis to preserve a secure network operation

## Slide 6: Target: Creating an operational grid <-> market interaction model within a demanding environment
Optimize grid operation especially within areas of high DER-share to resolve network bottlenecks
Design grid <-> market interactions within the „orange regime“
Development of generic requirements for a mediating communication and service platform
Develop and use flexibility for the distribution grid to minimize grid expansions
Deliver recommendations for a future market design
GRID
MARKET

## Slide 7: The traffic light concept enhances current grid operation concepts on various levels
SYSTEM- &
ENVIRONMENTAL DATA
CONGESTION MANAGEMENT
STATE ESTIMATION
FLEXIBILITY
Availability of Flexibility?
Effect analysis on the Grid
Validation of Results
Call of Flexibility
per Retailer
Input Data
- Measuring Data
- Switching States
- Weather Data / Prognosis
- Historical Data - Schedules of Flexibility
- …
Flexibility
Grid security measures
Grid related measures
Calculation
Evaluation
Action required?
Determination

## Slide 8: By publishing the available power range, market participants are enabled to allocate flexibility best
As of today, most power management interventions are resulting in cutting RES
The determination of an individual, non-discriminatory power range per retail company is facilitating a optimal congestion management as each retailer is able to select suitable schedules of flexibility within his portfolio
Flexibility calls will be distributed non-discriminatory among all retail companies owning / operating flexibility within the involved grid topology
Due to unique call IDs, retail companies could perform secondary trading on their flexibility calls, to e.g. hold SLAs with customers
Flex-Limitation Call
Affected Metering Points
1
DE123456…
0,97
ABC
2
DE234567…
0,79
BCD
n
DE987654..
0  1
XYZ
ID
Sensitivity
+Data
Metering Point ID
Available Power Range
-3,71 MW
Pmin
+5,23 MW
Pmax
Call-ID
28169132
DSO
Period
Westnetz
From Until
Call-Information
ID
Sensitivität
+Daten
Zählpunktnr.
-3,71 MW
Pmin
+11,23 MW
Pmax
Randbedingungen 1
1
0,97
ABC
123456
n
0  1
XYZ
987654
ID
Sensitivität
+Daten
Zählpunktnr.
-3,71 MW
Pmin
+11,23 MW
Pmax
Randbedingungen
1
0,97
ABC
123456
n
0  1
XYZ
987654
ID
Sensitivity
+Data
Metering Point ID
-1,23 MW
Pmin
+0,23 MW
Pmax
1. Boundary Condition
1
0,93
ABC
DE123456…
n
0  1
XYZ
DE987654…

## Slide 9: A real-life demonstration will take place in an area with high penetration of RES
The demonstration consists of:
a field-test with real customers (~5 MW RES generation, ~ 1,5 MW load)
a simulation for anticipating future scenarios in the year 2035
The goal of the demonstration is
To validate all new operational concepts
Testing the solution in a real environment and pave the way for a large-scale rollout
Trigging discussions with similar projects and applications and promoting the results
7,5 MW maximum Load & 23,5 MW installed RES
Lengerich
Lange
Handrup
Wettrup
Gersten
UA Lengerich
2015
2016
2017
Demo