## Slide 2: SAVE project - Smart use of own produced electricity by SMEs : opportunities in agriculture
Marleen Gysen, Innovatiesteunpunt
Presentation by Jeroen Büscher, VITO/EnergyVille

## Slide 3
Content
Project SAVE
Sectoral approach
Battery energy storage in agriculture

## Slide 4
Content
Project SAVE
Sectoral approach
Battery energy storage in agriculture

## Slide 5
Why SAVE?

## Slide 6
Consumption  production
Maximum use of own produced electricity
  shift of electricity consumption
  buffering surplus energy with installed assets
  battery energy storage
Peak shaving

## Slide 7
Online QuickScan & other simulation tools
Demonstration sites
Consultancy & implementation at SMEs
Dissemination & training

## Slide 8
Content
Project SAVE
Sectoral approach
Battery energy storage in agriculture

## Slide 9
Importance of energy profiles
How much electricity is needed? When?
  Day/Night (energy tariff)
  Seasonal dependence
  Power peaks (in relation with peak capacity and energy tariff)
  Baseload
Determination of flexible electricity consumption

## Slide 10
Dairy farm
Chart: kW

## Slide 11
Fruit farm
Chart: kWh
| jan | feb | mrt | apr | mei | jun | jul | aug | sep | okt | nov | dec
 | 34152 | 35509 | 23426 | 11004 | 9143 | 6073 | 3836 | 30796 | 76539 | 61218 | 38721 | 33286

## Slide 12
Flexible processes
Cooling (buffer – indirect cooling)
Pumps
Hot water production
… (sector dependent)

## Slide 13
LEGEND
Red: not flexible
Green: flexible
Winning
Cooling (buffer)
Production warm water (buffer & shifting)
Lighting
Others
35°
10°
Pre-cooler
Heat-recuperation
20°
40°
4° (1-4°C)
80° (80-95°C)
(NR) Milk tank
(R) Ice bank
(R) Boiler
Cleaning tubes
Cleaning tank
Milk calving
Every 3 days empty tank
2x/day cooling
Continuous low cooling
(NR) Manure robot
Ground water pump
80°
80°
40°
2x/day
100 liter
2,5x/week
60 liter
2x/day
40 liter
Process
Bound. con.
Technology
Vacuum pump and milk pump
TL, led, high pressure
12 kWh/1000liter
1-6 kW
10 kWh/1000liter
1,5-3 kW
8-12 MWh/year
4-6 MWh/year (recup)
2 kW/200 l boiler
Control night tariff
Consumption and power

## Slide 14
Content
Project SAVE
Sectoral approach
Battery energy storage in agriculture

## Slide 15
Batteries in agriculture
Self-loading applications (e.g. feeders)
Electric vehicles
Battery energy storage

## Slide 16
Batteries in agriculture
Back up
Peak shaving
Increased self-consumption

## Slide 17
Simulations dairy farm
Energy consumption: 50.000 kWh/year
PV: 50 kWp
Battery: 20 kWh

## Slide 19
Simulations fruit farm
Energy consumption: 50.000 kWh/year
PV: 50 kWp
Battery: 20 kWh

## Slide 25
Demonstration site Inagro

## Slide 26
PV
45 000
35 000
18 000
8 000
10 000
Cooling, washing
Grid
in kWh/year

## Slide 27
Inverter: 3 x 4,6 kW
Battery: 3 x 6,9 kWh
  3 kWh for back up
  17,7 kWh for increasing self-consumption
Off grid: some consumption will be switched off
Battery system

## Slide 28
Main lessons learned
A lot of interest – a lot of questions
Very hard to come up with a generic solution
Barriers:
  Lack of knowledge on technical potential of DSM + storage
  Lack of knowledge on investment costs and risks
  Training for technical installers

## Slide 29
Next project steps
Running 3 demonstration sites
  Showing working principles
  Create confidence for different sectors
Advanced exercise on economical value of DSM + storage for SME’s
No need for extra R&I activities at this level
  Required technology is there
  Energy management solutions on the market
  It’s more about bridging the gap between addressable market and technology

## Slide 30
Deployment prospects
QuickScan tool + handbook for SME’s
  First advice on DSM + storage possibilities
  Online
  Regional/sectoral workshops
Training for installers

## Slide 31
More info?
marleen.gysen@innovatiesteunpunt.be
www.innovatiesteunpunt.be
www.slimaansturenvanelektriciteit.be
@IWTSAVE